## Slide 1
Welcome to
CSA2002 INTRODUCTION TO DRONES
G.GANESAN, B.E (CSE)., M.E (CSE)., M.S(IT).,MISTE.,
SENIOR TEACHING FELLOW,
SCHOOL OF CSE.
+91-9500234437
ganesan.g@vitbhopal.ac.in

## Slide 2: Course Content
Date: 01, 06-02-2023 Time: 10.05am – 11.35am
Building Mission Control Drones using Drones
2. Building Mission Control Drones using Delivery Man

## Slide 3: Mission-1: Surveying with a Drone
Step-1: Prepare the Drone for flying using ArduPilot. No hardware changes
Step-2: Open the MissionPlanner software:
a. Go to the Config/Tuning page.
b. Select Planner.
Now we will see the following page.

## Slide 4: Surveying with a Drone
The green pointer is the Home/H. Hover the mouse over it, click and
move the pointer anywhere we want.

## Slide 5: Surveying with a Drone
Step-3: Place the pointer from where we will depart the drone to our
destination.
RTL1= (x1,y1) (x2,y2) (x3,y3) (x4,y4)
Step-4: Return to Launch (RTL): In WayPoints select the RTL option.
This is used to survey the areas which are pointed and return to
the launched place.
Step-5: Click “Add Below” on the WayPoints Panel, then we will see a new
waypoint.
Step-6: Click Command menu and Select the RETURN_TO_LAUNCH
option.

## Slide 6: Surveying with a Drone

## Slide 7: Surveying with a Drone

## Slide 8: Surveying with a Drone
Step-7: Give a name to the waypoint file and save it. We can reuse the
waypoint by “Load WP File” on the right-side of the screen.
Step-8: We can change the type of the Map and add some extra features
to the Map from the right-side of the map.

## Slide 9: Surveying with a Drone

## Slide 10: Surveying with a Drone
Step-9: Load the mission to ArduPilot by
a. Connecting the drone to the computer via telemetry or USB
cable.
b. Check the correct COM port or select the Auto mode.
c. Click on “Connect” button and select “Load WP File” from the
right-side of the map (or right click on the map).
d. Select the WP file and Hit the “Write WPs” button.
Now, we will see a pop-up message. The copter will ready to fly.

## Slide 11: Surveying with a Drone

## Slide 12: Surveying with a Drone
Step-10: Take the drone to the place where we select the Home/H point.
Step-11: The timing of hovering depends on the speed selected on
Config/Tuning page.
Step-12: Arm it as Auto mode.
a. Go to Config/Tuning  select Flight Mode.
The drone will survey the WayPoints and come the Home.
Now, we can change any mode and hit the Save Modes button then
Fly the drone.

## Slide 13: Mission-2: Delivery Man

## Slide 14: Delivery Man
Aim: Ship or Drop a Package to a Destination by the Drone.
- using Mission Planner Software
Modify the camera shutter button to drop a package from out drone.
- Connect a Servo motor with ArduPilot.
- Trigger a signal to the channel for connect and move the
servo motor.
- If the Placeholder connected to the Servo, we can drop the package
from the placeholder by triggering the servo from our remote
or the Mission Planner Software.

## Slide 15: Using Drones and Delivery Man
Step-1: Connect the Servo motor.
- Use the ArduPilot one-four output channels.

## Slide 16: Using Drones and Delivery Man
Step-2: Connect the Camera Gimbal.
- In Mission Planner Softwre, Select Optional Hardware and
Camera Gimbal.

## Slide 17: Using Drones and Delivery Man

## Slide 18: Using Drones and Delivery Man
Step-3: Configure the WayPoint
- Select a waypoint from the “Flight Plan” menu.
- Click “Add Below” button.
- Now we will see the “RETURN_TO_LAUNCH”
- Save the “WayPoint” file and write it to ArduPilot.
Step-4: Attach the Package
- Attach the package in Gimbal.
Step-5: When Gimbal is triggered by the Servo, the package falls.
The drone return to the launch point which described in waypoint.

## Slide 19: Using Drones and Delivery Man

## Slide 20: Communicate the Drone via ESP8266

## Slide 21: Communicate the Drone via ESP8266
Aim: To aware of the weather and the environment for a flight and mission.
Soln: Monitor the weather surrounding the drone by look at the air pressure
Requirements:
- A barometric pressure sensor (BMP 180 preferred)
- An Arduino (pro mini preferred)
- An ESP8266 transceiver module.

## Slide 22: Communicate the Drone via ESP8266
Step-1: Configure the Arduino with Barometer Sensor.
Arduino | Barometer Sensor
GND | GND
VCC | VCC
A4 | SCL
A5 | SDA

## Slide 23: Communicate the Drone via ESP8266

## Slide 24: Communicate the Drone via ESP8266
Step-2: Configure the Battery (3.3V) to the ESP8266.
Step-3: Download and Install barometer, ESP8266WiFi Libraries to
Arduino/libraries folder.
ESP8266 | Power Supply
VCC | 3.3 V
GND | GND
CH_PHD | 3.3 V

## Slide 25: Communicate the Drone via ESP8266
Step-4: Define the drone’s Altitude to get correct pressure data.
#define ALTITUDE
Step-5: Declare the hardware as follows:
SFE_BMP180 bmp180;
Esp8266EasyIoT esp;
Step-6: To see temperature, pressure, and forecast in the server, define
Esp8266EasyIoTMsg msgTemp(CHILD_ID_TEMP, V_TEMP);
Esp8266EasyIoTMsg msgPress(CHILD_ID_BARO, V_PRESSURE);
Esp8266EasyIoTMsg msgForec(CHILD_ID_BARO, V_FORECAST);

## Slide 26: Communicate the Drone via ESP8266
Step-7: Setting Baud rates for the ESP8266. For debugging on the serial
monitor, add another Baud rate.
void setup( )
Serial1.begin(9600);
Serial.begin(115200);
Step-8: Initialize the pressure sensor in the void setup( ) function, we need
to check the Barometer by adding a condition.
if (bmp180.begin() )
Serial.println(“BMP180 initialization successful”);
else {
Serial.println(“BMP180 initialization failed”);
while(1); }

## Slide 27: Communicate the Drone via ESP8266
Step-9: Save the module after adding the sensor parameters from the
temperature and pressure.
Step-10: Go to Config | User Info and set the “Instance ID” for the module.
Step-11: Upload the code to the Arduino and check the data shown in the
server from the Module list.

## Slide 28: Communicate the Drone via ESP8266

## Slide 29
Thank You
&
Queries?